## Slide 1: 8. SNMPv3
Objectives
Architecture
Security, Access Control
Message Format
Engine Discovery
Key Management
Hands On

## Slide 2: SNMPv3 changes
Modular Architecture
Security
Access Control
New Message Format
Administration

## Slide 3: RFCs
RFC 3410: Introduction
RFC 3411: Architecture
RFC 3412: Message Processing / Dispatch
RFC 3413: SNMP Applications
RFC 3414: Security (USM)
RFC 3415: Access Control (VACM)

## Slide 4: SNMPv3 reuses
Protocol Operations
Transport Protocol
Data Description Language
MIBs

## Slide 5: RFCs
RFC 3416: Protocol Operations
RFC 3417: Transport Mappings
RFC 2578: SMIv2
RFC 2579: Textual Conventions
RFC 2580: Conformance Statements

## Slide 6: SNMPv3 - Modular Architecture
SNMP
Entity
SNMP
Engine
Message
Processing
Subsystem
Security
Subsystem
Dispatcher
Access Control
Subsystem
SNMP
Applications
Command
Generator
Notification
Originator
Proxy
Forwarder
Command
Responder
Notification
Receiver
Other

## Slide 7: SNMP Entity - Manager
Command
Generator
Notification
Receiver
Message Processing
Subsystem
v1MP
v2cMP
PDU
Dispatcher
otherMP
v3MP
Security
Subsystem
Message
Dispatcher
Transport
Mapping
User-based
Security
Model
Other
Security
Model
UDP
IPX
Other
. . .
Network

## Slide 8: SNMP Entity - Agent
Message Processing
Subsystem
v1MP
v2cMP
PDU
Dispatcher
otherMP
v3MP
Security
Subsystem
Message
Dispatcher
Transport
Mapping
User-based
Security
Model
Other
Security
Model
UDP
IPX
Other
. . .
Network
Access Control
Subsystem
View-based
Access Control
Model
Other
Access Control
Model
Command
Responder
Proxy
Forwarder
Notification
Originator
MIB Instrumentation

## Slide 9: Security Requirements
Secure against
- Modification of Information
- Masquerade
- Message Stream Modification
- Disclosure
Not Secure against
- Denial of Service
- Traffic Analysis

## Slide 10: Security Services 1(3)
?
Permit the operation?
- who requested the operation?
- is the message unaltered?
- is the message timely?

## Slide 11: Security Services 2(3)
?
- what objects are accessed?
- has the requester access rights
on these objects?

## Slide 12: Security Services 3(3)
?
Message encryption?
- are we sending secret information?

## Slide 13: Security Levels
Three Levels:
- no authentication / no privacy
- authentication / no privacy
- authentication / privacy
Examples
- Monitoring: noAuth / noPriv
- Configuration: Auth / noPriv
- Accounting Data: Auth / Priv

## Slide 14: Message Structure
msgVersion
msgID
msgMaxSize
msgFlags
msgSecurityModel
msgAuthoritativeEngineID
msgAuthoritativeEngineBoots
msgAuthoritativeEngineTime
msgUserName
msgAuthenticationParameters
msgPrivacyParameters
contextEngineID
contextName
PDU
Scoped PDU
(plaintext or
encrypted)
Generated/
Processed by
User Security
Model (USM)
Generated/
Processed by
Message
Processing
Model
scope of authentication
scope of encryption

## Slide 15: Message Transmission
Retrieve user information
Privacy
required?
Encrypt scopedPdu
set msgPrivacyParameters
msgPrivacyParameters
 null string
Authentication
required?
Compute MAC
set msgAuthenticationParameters
msgAuthenticationParameters
 null string
YES
YES
NO
NO

## Slide 16: Message Reception
Retrieve message parameters
Authentication
required?
Dencrypt scopedPdu
Determine if message is within time window
Privacy
required?
Compute MAC; compare to
msgAuthenticationParameters
YES
YES
NO
NO

## Slide 17: Engine ID 1(2)
Administratively unique identifier
Format
- OCTET STRING; 5-32 byte long
- 1st bit = 0  Enterprise Method
- 1st bit = 1  Standard Method
Enterprise Method (cisco)
- the first 4 bytes are set to private enterprise
number (00000009)
- the following 8 bytes are assigned in an enterprise-
specific method (mac address + 2 random bytes)

## Slide 18: Engine ID 2(2)
Standard Method (cisco)
- the first 4 bytes are set to private enterprise
number (80000009)
- the 5th byte indicate how the rest are used:
0 – reserved 4 – admin text value
1 – IPv4 address 5 – admin hex value
2 – IPv6 address 6...127 – reserved
3 – MAC address 128...255 – enterprise specific

## Slide 19: Reports
A new PDU for Engine to Engine communiction
All messages that can be responded to
are reportable
Gives the sender a change to send a
correct request
Used for discovery and synchronization
Var-Bind: OID and single value indicating
the problem

## Slide 20: Timeliness
Manager needs to keep track of
EngineBoot/Time in the Agent
Agent checks EngineBoot/Time
- wrong value >> report message
Default limit is 150 s

## Slide 21: Key Management
Shared secret keys
1 key for authentication
1 key for privacy
Initial setup outside SNMPv3
Not accessible via SNMP
Key Localization Process

## Slide 22: Key Localization Process
User Password
Expand to 220
User Key
MD5 (16-octet key)
SHA-1 (20-octet key)
H(User Password)
Localized Key
H(User Key+
Remote EngineID+
User Key)
Localized Key
H(User Key+
Remote EngineID+
User Key)
Localized Key
H(User Key+
Remote EngineID+
User Key)
. . . . .

## Slide 23: Agent Discovery
Two step discovery depending
on snmpSecurityLevel
NoAuth/NoPriv
- snmpEngineID
Auth/NoPriv or Auth/Priv
- snmpEngineBoots
- snmpEngineTime

## Slide 24: Discovery – NoAuth/NoPriv 1(4)
---------- Get Request ----------
Version = 3
Id = 4
Maximum size = 65520
Message flags = 04
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .1.. = reportableFlag is on
Security model = 3
Authoritative engine id = NULL
Authoritative engine boots = 0
Authoritative engine time = 0
User name = NULL
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = NULL
Context name = NULL
Command = Get request
Request ID = 3
Error status = 0 (No error)
Error index = 0
No varBindList

## Slide 25: Discovery – NoAuth/NoPriv 2(4)
------------- Report -------------
Version = 3
Id = 4
Maximum size = 2048
Message flags = 00
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .0.. = reportableFlag is off
Security model = 3
Authoritative engine id= 00000009020000D006024BF4
Authoritative engine boots = 23
Authoritative engine time = 248073
User name = NULL
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF4
Context name = NULL
Command = Report
Request ID = 3
Error status = 0 (No error)
Error index = 0
Object = internet.6.3.15.1.1.4.0
Value = 17 (counter)

## Slide 26: Discovery – NoAuth/NoPriv 3(4)
---------- Get Request ----------
Version = 3
Id = 5
Maximum size = 65520
Message flags = 04
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .1.. = reportableFlag is on
Security model = 3
Authoritative engine id = 00000009020000D006024BF4
Authoritative engine boots = 0
Authoritative engine time = 0
User name = oper1
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF4
Context name = NULL
Command = Get request
Request ID = 4
Error status = 0 (No error)
Error index = 0
Object = mib-2.1.3.0
Value = NULL

## Slide 27: Discovery – NoAuth/NoPriv 4(4)
------------- Response -------------
Version = 3
Id = 5
Maximum size = 2048
Message flags = 00
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .0.. = reportableFlag is off
Security model = 3
Authoritative engine id= 00000009020000D006024BF4
Authoritative engine boots = 23
Authoritative engine time = 248073
User name = oper1
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF4
Context name = NULL
Command = Response
Request ID = 4
Error status = 0 (No error)
Error index = 0
Object = mib-2.1.3.0
Value = 24807356

## Slide 28: Discovery – Auth/NoPriv 1(6)
---------- Get Request ----------
Version = 3
Id = 5
Maximum size = 65520
Message flags = 04
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .1.. = reportableFlag is on
Security model = 3
Authoritative engine id = NULL
Authoritative engine boots = 0
Authoritative engine time = 0
User name = NULL
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = NULL
Context name = NULL
Command = Get request
Request ID = 4
Error status = 0 (No error)
Error index = 0
No varBindList

## Slide 29: Discovery – Auth/NoPriv 2(6)
------------- Report -------------
Version = 3
Id = 5
Maximum size = 1500
Message flags = 00
.... ...0 = authFlag is off
.... ..0. = privFlag is off
.... .0.. = reportableFlag is off
Security model = 3
Authoritative engine id= 00000009020000D006024BF5
Authoritative engine boots = 1
Authoritative engine time = 1296955
User name = NULL
Authentication parameters = NULL
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF5
Context name = NULL
Command = Report
Request ID = 4
Error status = 0 (No error)
Error index = 0
Object = internet.6.3.15.1.1.4.0
Value = 6 (counter)

## Slide 30: Discovery – Auth/NoPriv 3(6)
---------- Get Request ----------
Version = 3
Id = 6
Maximum size = 65520
Message flags = 05
.... ...1 = authFlag is on
.... ..0. = privFlag is off
.... .1.. = reportableFlag is on
Security model = 3
Authoritative engine id = 00000009020000D006024BF5
Authoritative engine boots = 0
Authoritative engine time = 0
User name = admin1
Authentication parameters = [<0E>y<12>r!ECAu y
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF5
Context name = NULL
Command = Get request
Request ID = 5
Error status = 0 (No error)
Error index = 0
Object = mib-2.1.3.0
Value = NULL

## Slide 31: Discovery – Auth/NoPriv 4(6)
------------- Report -------------
Version = 3
Id = 6
Maximum size = 1500
Message flags = 01
.... ...1 = authFlag is on
.... ..0. = privFlag is off
.... .0.. = reportableFlag is off
Security model = 3
Authoritative engine id= 00000009020000D006024BF5
Authoritative engine boots = 1
Authoritative engine time = 1296955
User name = admin1
Authentication parameters = 3^qN<09>NCg<0B1A>v
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF5
Context name = NULL
Command = Report
Request ID = 5
Error status = 0 (No error)
Error index = 0
Object = internet.6.3.15.1.1.2.0
Value = 15 (counter)

## Slide 32: Discovery – Auth/NoPriv 5(6)
---------- Get Request ----------
Version = 3
Id = 7
Maximum size = 65520
Message flags = 05
.... ...1 = authFlag is on
.... ..0. = privFlag is off
.... .1.. = reportableFlag is on
Security model = 3
Authoritative engine id = 00000009020000D006024BF5
Authoritative engine boots = 1
Authoritative engine time = 1296955
User name = admin1
Authentication parameters = [<0E>y<12>r!ECAu y
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF5
Context name = NULL
Command = Get request
Request ID = 6
Error status = 0 (No error)
Error index = 0
Object = mib-2.1.3.0
Value = NULL

## Slide 33: Discovery – Auth/NoPriv 6(6)
------------- Response -------------
Version = 3
Id = 7
Maximum size = 1500
Message flags = 01
.... ...1 = authFlag is on
.... ..0. = privFlag is off
.... .0.. = reportableFlag is off
Security model = 3
Authoritative engine id= 00000009020000D006024BF5
Authoritative engine boots = 1
Authoritative engine time = 1296955
User name = admin1
Authentication parameters = oMpJ<1E>aWbf-$
Privacy parameters = NULL
Context engine id = 00000009020000D006024BF5
Context name = NULL
Command = Response
Request ID = 6
Error status = 0 (No error)
Error index = 0
Object = mib-2.1.3.0
Value = 129695850

## Slide 34: ASI – Command Generator
Command
Generator/
Notification
Originator
Dispatcher
Message
Processing
Model
Security Model
sendPdu
prepareOutgoingMsg
generateRequestMsg
Send SNMP Req
Msg to Network
Receive SNMP Resp
Msg from Network
prepareDataElements
processIncomingMsg
processResponsePdu

## Slide 35: sendPdu
Command
Generator/
Notification
Originator
Dispatcher
Message
Processing
Model
Security Model
sendPdu
prepareOutgoingMsg
generateRequestMsg
Send SNMP Req
Msg to Network
statusInformation =
sendPdu(
IN transportDomain
IN transportAddress
IN messageProcessingModel
IN securityModel
IN securityName
IN securityLevel
IN contextEngineID
IN contextName
IN pduVersion
IN PDU
IN expectResponse
)

## Slide 36: prepareOutgoingMsg
prepareOutgoingMessage(
IN transportDomain
IN transportAddress
IN messageProcessingModel
IN securityModel
IN securityName
IN securityLevel
IN contextEngineID
IN contextName
IN pduVersion
IN PDU
IN expectResponse
IN sendPduHandle
OUT destTransportDomain
OUT destTransportAddress
OUT outgoingMessage
OUT outgoingMessageLength
)
Command
Generator/
Notification
Originator
Dispatcher
Message
Processing
Model
Security Model
sendPdu
prepareOutgoingMsg
generateRequestMsg
Send SNMP Req
Msg to Network

## Slide 37: generateRequestMsg
statusInformation =
generateRequestMsg(
IN messageProcessingModel
IN globalData
IN maxMessageSize
IN securityModel
IN securityEngineID
IN securityName
IN securityLevel
IN scopedPDU
OUT securityParameters
OUT wholeMsg
OUT wholeMsgLength
)
Command
Generator/
Notification
Originator
Dispatcher
Message
Processing
Model
Security Model
sendPdu
prepareOutgoingMsg
generateRequestMsg
Send SNMP Req
Msg to Network

## Slide 38: ASI – Command Responder
Command
Responder
Dispatcher
Message
Processing
Model
Security Model
registerContextEngineID
processIncomingMsg
Send SNMP Resp
Msg to Network
Receive SNMP Req
Msg from Network
processPdu
returnResponsePdu
prepareDataElements
generateResponsetMsg
prepareResponseMsg

## Slide 39: registerContextEngineID
Command
Responder
Dispatcher
Message
Processing
Model
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Req
Msg from Network
processPdu
prepareDataElements
statusInformation =
registerContextEngineID(
IN contextEngineID
IN pduType
)

## Slide 40: prepareDataElements
result =
prepareDataElements(
IN transportDomain
IN transportAddress
IN wholeMsg
IN wholeMsgLength
OUT messageProcessingModel
OUT securityModel
OUT securityName
OUT securityLevel
OUT contextEngineID
OUT contextName
OUT pduVersion
OUT PDU
OUT pduType
OUT sendPduHandle
OUT maxSizeResponseScopedPDU
OUT statusInformation
OUT stateReference
)
Command
Responder
Dispatcher
Message
Processing
Model
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Req
Msg from Network
processPdu
prepareDataElements

## Slide 41: processIncomingMsg
statusInformation =
processIncomingMsg(
IN messageProcessingModel
IN maxMessageSize
IN securityParameters
IN securityModel
IN securityLevel
IN wholeMsg
IN wholeMsgLength
OUT securityEngineID
OUT securityName
OUT scopedPDU
OUT maxSizeResponseScopedPDU
OUT securityStateReference
)
Command
Responder
Dispatcher
Message
Processing
Model
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Req
Msg from Network
processPdu
prepareDataElements

## Slide 42: processPdu
processPdu (
IN messageProcessingModel
IN securityModel
IN securityName
IN securityLevel
IN contextEngineID
IN contextName
IN pduVersion
IN PDU
IN maxSizeResponseScopedPDU
IN stateReference
)
Command
Responder
Dispatcher
Message
Processing
Model
Security Model
registerContextEngineID
processIncomingMsg
Receive SNMP Req
Msg from Network
processPdu
prepareDataElements

## Slide 43: View-based Access Control Model
vacmViewTreeFamilyTable
vacmAccessTable
vacmContextTable
where
how
why
what
which
vacmSecurityToGroupTable
who
securityModel
securityName
contextName
securityModel
securityLevel
groupName
viewType
(read/
write/
notify)
viewName
Yes/No
object-type
object-instance
variableName (OID)

## Slide 44: Administration 1(2)
iso(1).org(3).dod(6).internet(1).snmpV2(6).snmpModules(3)
SNMPv2-MIB
SNMP-FRAMEWORK-MIB
SNMP-MPD-MIB
SNMP-TARGET-MIB
SNMP-COMMUNITY-MIB
SNMP-VIEW-BASED-VACM-MIB
SNMP-USER-BASED-SM-MIB
SNMP-NOTIFICATION-MIB
SNMP-PROXY-MIB

## Slide 45: Administration 2(2)
mgmt
private
snmpV2
snmpDomains
snmpProxies
snmpModules
snmpMIB
snmpFrameworkMIB
snmpMPDMIB
snmpTargetMIB
snmpCommunityMIB
snmpVacmMIB
snmpUsmMIB
snmpNotificationMIB
snmpProxyMIB

## Slide 46: Trap Notification – Cisco CLI
#show config
!
snmp-server engineID local 00000009020000D006024BF4
snmp-server user oper1 opergr1 v3
snmp-server user admin1 admingr1 v3 auth md5
snmp-server group opergr1 v3 noauth read level-2
snmp-server group admingr1 v3 auth read level-2 write level-2
snmp-server view level-1 system included
snmp-server view level-1 interfaces included
snmp-server view level-2 internet included
snmp-server community ardbeg view level-1 RO
snmp-server community bowmore view level-1 RW
snmp-server location Floor 2
snmp-server contact Leif Hagman
snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart
snmp-server enable traps tty
snmp-server host 192.10.20.4 public snmp

## Slide 47: Notify and Target Tables 1(2)
1
2
Notify Table
Send all events
as traps to receiver
trap.
Target Table
Use IP/UDP and send to 192.10.20.4 on port 162.
Params Table
SNMPv1 message with community string public.

## Slide 48: Notify and Target Tables 2(2)
1
2
3
4
Filter Table
All traps except ciscoTelnetTrap.

## Slide 49: User Setup – Cisco CLI
#show config
!
snmp-server engineID local 00000009020000D006024BF4
snmp-server user oper1 opergr1 v3
snmp-server user admin1 admingr1 v3 auth md5
snmp-server group opergr1 v3 noauth read level-2
snmp-server group admingr1 v3 auth read level-2 write level-2
snmp-server view level-1 system included
snmp-server view level-1 interfaces included
snmp-server view level-2 internet included
snmp-server community ardbeg view level-1 RO
snmp-server community bowmore view level-1 RW
snmp-server location Floor 2
snmp-server contact Leif Hagman
snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart
snmp-server enable traps tty
snmp-server host 192.10.20.4 public snmp

## Slide 50: USM Tables

## Slide 51: VACM Setup – Cisco CLI
#show config
!
snmp-server engineID local 00000009020000D006024BF4
snmp-server user oper1 opergr1 v3
snmp-server user admin1 admingr1 v3 auth md5
snmp-server group opergr1 v3 noauth read level-2
snmp-server group admingr1 v3 auth read level-2 write level-2
snmp-server view level-1 system included
snmp-server view level-1 interfaces included
snmp-server view level-2 internet included
snmp-server community ardbeg view level-1 RO
snmp-server community bowmore view level-1 RW
snmp-server location Floor 2
snmp-server contact Leif Hagman
snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart
snmp-server enable traps tty
snmp-server host 192.10.20.4 public snmp

## Slide 52: VACM Tables 1(2)

## Slide 53: VACM Tables 2(2)