## Slide 1: 2. SNMP Protocol
Objectives
Languages: ASN.1, SMI, BER
Name Space, OIDs
MIB-Objects and Traps
Protocol Operations
SNMPv3
Exercise

## Slide 2: SNMP Architecture
User interface
Network management application
Agent
MIB
Agent
Agent
Managed
device
SNMP
NMS
SNMP
SNMP
MIB
Managed
device
MIB
Managed
device

## Slide 3: Retrieve Information
1. What information exist?
2. How to ask?

## Slide 4: SNMP Protocol Encoding
The Goal is to transfer (management) information between heterogeneous systems via a well-understood and machine-independent syntax
Machines vary by
- word size: e.g. 8, 16, 32, 64, other
- arithmetic type: 1’s complement, 2’s complement
- byte ordering: big endian, little endian
- character set: ASCII, EBCDIC, 16 bit characters

## Slide 5: SNMP Language 1(2)
ASN.1 (Abstract Syntax Notation One)
- Machine independent language
- Comprehensive, complicated
- Described in spec. ITU X.208
- Easier move to CMIP
SMI (Structure of Management Information)
- Subset of ASN.1
- MIB Tree (name space)
- Common Object structure
- Generic Data types
- SMIv1 / SMIv2
ASN.1
ASN.1

## Slide 6: SNMP Language 2(2)
BER (Basic Encoding Rules)
- Coding Scheme
- ASN.1 to binary representation
- Described in spec. ITU X.209
BER

## Slide 7: MIB Tree 1(4)
iso
ccitt
joint-iso-ccitt
org
dod
internet
exper
mgmt
private

## Slide 8: MIB Tree 2(4)
exper
mgmt
private
mib-2
enterprises
interfaces
proteon
system
at
ifNumber
sysDescr
ifTable
ibm
ifEntry

## Slide 9: MIB Tree 3(4)
iso
ccitt
joint-iso-ccitt
org
dod
internet
exper
mgmt
private

## Slide 10: MIB Tree 4(4)
exper (3)
mgmt (2)
private (4)
mib-2
enterprises
interfaces
proteon
system
at
ifNumber
sysDescr
ifTable
ibm
ifEntry

## Slide 11: Interpret Information
010011101
How to interpret the answer?

## Slide 12: Data Representation
sysUpTime = 2 days, 10:05:02
sysUpTime = 36 days, 12:10:01
NMS
20 910 200
315 420 100
= 2 days, 10:05:02
= 36 days, 12:10:01
20 910 200
315 420 100

## Slide 13: Data Types – SMIv1 1(2)
Universal types
  INTEGER
  OCTET STRING
  OBJECT IDENTIFIER
  NULL
Application types
  IpAddress
  Counter
  Gauge
  TimeTicks
  Opaque

## Slide 14: Data Types – SMIv1 2(2)
Constructed types
  SEQUENCE
  SEQUENCE OF

## Slide 15: Data Types – SMIv2 1(2)
Universal types
  INTEGER
  OCTET STRING
  OBJECT IDENTIFIER
  NULL
Application types
  Integer32 -- same tag as INTEGER
  IpAddress
  Counter32
  Gauge32
  Unsigned32 -- same tag as Gauge32
  TimeTicks
  Counter64

## Slide 16: Data Types – SMIv2 2(2)
Pseudotypes
  BITS
Constructed types
  SEQUENCE
  SEQUENCE OF

## Slide 17: Data Access
SMIv1 - not-accessible
- read-only
- read-write
- write-only
SMIv2 - not-accessible
- accessible-for-notify
- read-only
- read-write
- read-create

## Slide 18: Status (requirement level)
SMIv1 - mandatory
- deprecated
- obsolete
SMIv2 - current
- deprecated
- obsolete

## Slide 19: Object Definition – SMIv1 1(2)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since
the network management portion of the system
was last re-initialized."
::= { system 3 }

## Slide 20: Object Definition – SMIv1 2(2)
ifAdminStatus OBJECT-TYPE
SYNTAX INTEGER {
up(1), -- ready to pass packets
down(2),
testing(3) -- in some test mode
}
ACCESS read-write
STATUS mandatory
DESCRIPTION
"The desired state of the interface. The
testing(3) state indicates that no operational
packets can be passed."
::= { ifEntry 7 }

## Slide 21: Trap Definition – SMIv1 1(2)
linkDown TRAP-TYPE
ENTERPRISE snmp
VARIABLES { ifIndex }
DESCRIPTION
"A linkDown trap signifies that the sending
protocol entity recognizes a failure in one of
the communication links represented in the
agent's configuration."
::= 2

## Slide 22: Trap Definition – SMIv1 2(2)
sysAlarm TRAP-TYPE
ENTERPRISE easysoft
VARIABLES { sysName, sysPri, sysMessage }
DESCRIPTION
"A sysAlarm trap signifies that a system or
service being monitored has not respond
against the configured poll criteria."
::= 12

## Slide 23: Object Definition – SMIv2 1(2)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"The time (in hundredths of a second) since
the network management portion of the system
was last re-initialized."
::= { system 3 }

## Slide 24: Object Definition – SMIv2 2(2)
serialDialoutTimeout OBJECT-TYPE
SYNTAX Integer32 (1..65535)
MAX-ACCESS read-create
STATUS current
DESCRIPTION
"This timeout value is used when the probe initiates
the serial connection with the intention of contacting
a management station. This variable represents the
number of seconds of inactivity allowed before
terminating the connection on this serial interface."
DEFVAL { 20 }
::= { serialConfigEntry 8 }

## Slide 25: Trap Definition – SMIv2 1(2)
linkDown NOTIFICATION-TYPE
OBJECTS { ifIndex, ifAdminStatus, ifOperStatus }
STATUS current
DESCRIPTION
"A linkDown trap signifies that the SNMPv2 entity,
acting in an agent role, has detected that the
ifOperStatus object for one of its communication
links is about to transition into the down state."
::= { snmpTraps 3 }

## Slide 26: Trap Definition – SMIv2 2(2)
sysAlarm NOTIFICATION-TYPE
OBJECTS { sysName, sysPri, sysMessage }
STATUS current
DESCRIPTION
"A sysAlarm trap signifies that a system or
service being monitored has not respond
against the configured poll criteria."
::= { easysoft 0 12 }

## Slide 27: Constructs in MIB Modules
SMIv1
  OBJECT-TYPE
  TRAP-TYPE
SMIv2
  MODULE-IDENTITY
  OBJECT-TYPE
  TEXTUAL-CONVENTION
  NOTIFICATION-TYPE
  OBJECT-IDENTITY
  OBJECT-GROUP
  NOTIFICATION-GROUP
  MODULE-COMPLIANCE
  AGENT-CAPABILITIES

## Slide 28: MODULE-IDENTITY
rmon MODULE-IDENTITY
LAST-UPDATED "9605270000Z"
ORGANIZATION "IETF RMON MIB Working Group"
CONTACT-INFO
"Steve Waldbusser (WG Editor)
Postal: International Network Services
650 Castro Street, Suite 260
Mountain View, CA 94041
Phone: +1 415 254 4251
Email: waldbusser@ins.com”
DESCRIPTION
"The MIB module for managing remote monitoring
device implementations. This MIB module
augments the original RMON MIB as specified in
RFC 1757."
::= { mib-2 16 }

## Slide 29: TEXTUAL-CONVENTION
PositiveInteger ::= TEXTUAL-CONVENTION
DISPLAY-HINT "d"
STATUS current
DESCRIPTION
"This data type is a non-zero and
non-negative value."
SYNTAX INTEGER (1..2147483647)

## Slide 30: MIB Module
<module name> DEFINITIONS ::= BEGIN
<linkage>
<declarations>
END

## Slide 31: SMIv1 Base Module
RFC1155-SMI DEFINITIONS ::= BEGIN
EXPORTS -- EVERYTHING
internet, directory, mgmt,
experimental, private, enterprises,
OBJECT-TYPE, ObjectName, ObjectSyntax,
SimpleSyntax, ApplicationSyntax, NetworkAddress,
IpAddress, Counter, Gauge, TimeTicks, Opaque;
-- the path to the root
internet OBJECT IDENTIFIER ::= { iso org(3) dod(6) 1 }
directory OBJECT IDENTIFIER ::= { internet 1 }
mgmt OBJECT IDENTIFIER ::= { internet 2 }
experimental OBJECT IDENTIFIER ::= { internet 3 }
private OBJECT IDENTIFIER ::= { internet 4 }
enterprises OBJECT IDENTIFIER ::= { private 1 }
…

## Slide 32: SMIv2 Base Module
SNMPv2-SMI DEFINITIONS ::= BEGIN
-- the path to the root
org OBJECT IDENTIFIER ::= { iso 3 } -- "iso" = 1
dod OBJECT IDENTIFIER ::= { org 6 }
internet OBJECT IDENTIFIER ::= { dod 1 }
directory OBJECT IDENTIFIER ::= { internet 1 }
mgmt OBJECT IDENTIFIER ::= { internet 2 }
mib-2 OBJECT IDENTIFIER ::= { mgmt 1 }
transmission OBJECT IDENTIFIER ::= { mib-2 10 }
experimental OBJECT IDENTIFIER ::= { internet 3 }
private OBJECT IDENTIFIER ::= { internet 4 }
enterprises OBJECT IDENTIFIER ::= { private 1 }
security OBJECT IDENTIFIER ::= { internet 5 }
snmpV2 OBJECT IDENTIFIER ::= { internet 6 }
…

## Slide 33: MIB-II Module
system
11 Groups
interfaces
at
ip
icmp
tcp
udp
egp
cmot
transmission
snmp

## Slide 34: MIB-II (SMIv1) 1(3)
RFC1213-MIB DEFINITIONS ::= BEGIN
IMPORTS
mgmt, NetworkAddress, IpAddress, Counter, Gauge,
TimeTicks
FROM RFC1155-SMI
OBJECT-TYPE
FROM RFC-1212;
-- This MIB module uses the extended OBJECT-TYPE macro as
-- defined in [14];
-- MIB-II (same prefix as MIB-I)
mib-2 OBJECT IDENTIFIER ::= { mgmt 1 }

## Slide 35: MIB-II 2(3)
-- textual conventions
DisplayString ::=
OCTET STRING
-- This data type is used to model textual information taken
-- from the NVT ASCII character set. By convention, objects
-- with this syntax are declared as having
-- SIZE (0..255)
PhysAddress ::=
OCTET STRING
-- This data type is used to model media addresses. For many
-- types of media, this will be in a binary representation.
-- For example, an Ethernet-address would be represented as
-- a string of 6 octets.

## Slide 36: MIB-II 3(3)
-- groups in MIB-II
system OBJECT IDENTIFIER ::= { mib-2 1 }
interfaces OBJECT IDENTIFIER ::= { mib-2 2 }
at OBJECT IDENTIFIER ::= { mib-2 3 }
ip OBJECT IDENTIFIER ::= { mib-2 4 }
icmp OBJECT IDENTIFIER ::= { mib-2 5 }
tcp OBJECT IDENTIFIER ::= { mib-2 6 }
udp OBJECT IDENTIFIER ::= { mib-2 7 }
egp OBJECT IDENTIFIER ::= { mib-2 8 }
-- historical (some say hysterical)
-- cmot OBJECT IDENTIFIER ::= { mib-2 9 }
transmission OBJECT IDENTIFIER ::= { mib-2 10 }
snmp OBJECT IDENTIFIER ::= { mib-2 11 }

## Slide 37: MIB-II system 1(5)
-- the System group
-- Implementation of the System group is mandatory for all
-- systems. If an agent is not configured to have a value
-- for any of these variables, a string of length 0 is
-- returned.
sysDescr OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A textual description of the entity. This value should include the full name and version-identification of the system's hardware type, software operating-system and networking software. It is mandatory that this only contains printable ASCII characters."
::= { system 1 }

## Slide 38: MIB-II system 2(5)
sysObjectID OBJECT-TYPE
SYNTAX OBJECT IDENTIFIER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The vendor's authoritative identification of the
network management subsystem contained in the
entity. This value is allocated within the SMI
enterprises subtree (1.3.6.1.4.1) and provides an
easy and unambiguous means for determining `what
kind of box' is being managed. For example, if
vendor `Flintstones, Inc.' was assigned the
subtree 1.3.6.1.4.1.4242, it could assign the
identifier 1.3.6.1.4.1.4242.1.1 to its `Fred
Router'."
::= { system 2 }

## Slide 39: MIB-II system 3(5)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the
network management portion of the system was last
re-initialized."
::= { system 3 }

## Slide 40: MIB-II system 4(5)
sysContact OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-write
STATUS mandatory
DESCRIPTION
"The textual identification of the contact person
for this managed node, together with information
on how to contact this person."
::= { system 4 }

## Slide 41: MIB-II system 5(5)
sysName OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-write
STATUS mandatory
DESCRIPTION
"An administratively-assigned name for this
managed node. By convention, this is the node's
fully-qualified domain name."
::= { system 5 }

## Slide 42: MIB-II interfaces 1(6)
ifNumber OBJECT-TYPE
SYNTAX INTEGER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The number of network-interfaces (regardless of
their current state) present on this system."
::= { interfaces 1 }

## Slide 43: MIB-II interfaces 2(6)
-- the Interfaces table
-- The Interfaces table contains information on the entity's
-- interfaces.
ifTable OBJECT-TYPE
SYNTAX SEQUENCE OF IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"A list of interface-entries. The number of
entries is given by the value of ifNumber."
::= { interfaces 2 }

## Slide 44: MIB-II interfaces 3(6)
ifEntry OBJECT-TYPE
SYNTAX IfEntry
ACCESS not-accessible
STATUS mandatory
DESCRIPTION
"An interface entry containing objects at the
subnetwork-layer and below for a particular
interface."
INDEX { ifIndex }
::= { ifTable 1 }

## Slide 45: MIB-II interfaces 4(6)
IfEntry ::=
SEQUENCE {
ifIndex
INTEGER,
ifDescr
DisplayString,
ifType
INTEGER,
…
ifSpecific
OBJECT IDENTIFIER
}

## Slide 46: MIB-II interfaces 5(6)
ifIndex OBJECT-TYPE
SYNTAX INTEGER
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A unique value for each interface. Its value
ranges between 1 and the value of ifNumber. The
value for each interface must remain constant at
least from one re-initialization of the entity's
network management system to the next re-
initialization."
::= { ifEntry 1 }

## Slide 47: MIB-II interfaces 6(6)
ifDescr OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
ACCESS read-only
STATUS mandatory
DESCRIPTION
"A textual string containing information about the
interface. This string should include the name of
the manufacturer, the product-name and the version
of the hardware-interface."
::= { ifEntry 2 }

## Slide 48: UPS (SMIv2) 1(4)
UPS-MIB DEFINITIONS ::= BEGIN
IMPORTS
MODULE-IDENTITY, OBJECT-TYPE, NOTIFICATION-TYPE,
OBJECT-IDENTITY, Counter32, Gauge32, Integer32
FROM SNMPv2-SMI
DisplayString, TimeStamp, TimeInterval, TestAndIncr,
AutonomousType, TEXTUAL-CONVENTION
FROM SNMPv2-TC
MODULE-COMPLIANCE, OBJECT-GROUP
FROM SNMPv2-CONF
mib-2
FROM RFC1213-MIB;

## Slide 49: UPS 2(4)
upsMIB MODULE-IDENTITY
LAST-UPDATED "9402230000Z"
ORGANIZATION "IETF UPS MIB Working Group"
CONTACT-INFO
"Jeffrey D. Case
Postal: SNMP Research, Incorporated
3001 Kimberlin Heights Road
Knoxville, TN 37920
US
Tel: +1 615 573 1434
Fax: +1 615 573 9197
E-mail: case@snmp.com"
DESCRIPTION
"The MIB module to describe Uninterruptible Power
Supplies."
::= { mib-2 33 }

## Slide 50: UPS 3(4)
PositiveInteger ::= TEXTUAL-CONVENTION
DISPLAY-HINT "d"
STATUS current
DESCRIPTION
"This data type is a non-zero and non-negative value."
SYNTAX INTEGER (1..2147483647)
NonNegativeInteger ::= TEXTUAL-CONVENTION
DISPLAY-HINT "d"
STATUS current
DESCRIPTION
"This data type is a non-negative value."
SYNTAX INTEGER (0..2147483647)

## Slide 51: UPS upsIdent 4(4)
upsObjects OBJECT IDENTIFIER ::= { upsMIB 1 }
-- The Device Identification group.
-- All objects in this group except for upsIdentName and
-- upsIdentAttachedDevices are set at device initialization
-- and remain static.
upsIdent OBJECT IDENTIFIER ::= { upsObjects 1 }
upsIdentManufacturer OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..31))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"The name of the UPS manufacturer."
::= { upsIdent 1 }

## Slide 52: SNMP – Architecture
PROTOCOLS
TELNET | SMTP | F TP | NFS | T F T P | SNMP
TCP | UDP
IP, ICMP, GGP, EGP
ARP
Ethernet IEEE 802.x PSDN (X.25)
Network
Transport
Physical
Data Link
Session
Presentation
Application
OSI

## Slide 53: SNMPv1 – Protocol Operations

## Slide 54: SNMPv2 – Protocol Operations
Get-Request
GetNext-Request
Set-Request
Response
Trap

## Slide 55: SNMPv1 – Get Request PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
sysUpTime

## Slide 56: SNMPv1 – Response PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
sysUpTime

## Slide 57: SNMPv1 – GetNext Request PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
ifInOctets, ifOutOctets

## Slide 58: SNMPv1 – Response PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
ifInOctets, ifOutOctets

## Slide 59: SNMPv1 – Set Request PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
sysLocation

## Slide 60: SNMPv1 – Response PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
0
private
Resp
125
0
0
mib-2.1.6.0
OCTET STRING
Floor 3
sysLocation

## Slide 61: SNMPv1 – Trap PDU
Version | Community | PDU | Enterprise | Network Address | Gen Trap | Spec Trap | Time- Stamp | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
Authentication Failure

## Slide 62: SNMPv2 – GetBulk Request PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
ifInOctets, ifOutOctets ( 5 instances )

## Slide 63: SNMPv2 – Response PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | … | Objectn
Part 1
Part 2
Variable Bindings
Obj.ID | Type | Value
ifInOctets, ifOutOctets ( 5 instances )

## Slide 64: SNMPv2 – Trap/Inform PDU
Version | Community | PDU | Req.ID | Error Status | Error Index | Object1 | Object2 | …
Part 1
Part 2
Variable Bindings

## Slide 65: SNMPv3 - Architecture
SNMP
Entity
SNMP
Engine
Message
Processing
Subsystem
Security
Subsystem
Dispatcher
Access Control
Subsystem
SNMP
Applications
Command
Generator
Notification
Originator
Proxy
Forwarder
Command
Responder
Notification
Receiver
Other

## Slide 66: SNMP Entity - Manager
Command
Generator
Notification
Receiver
Message Processing
Subsystem
v1MP
v2cMP
PDU
Dispatcher
otherMP
v3MP
Security
Subsystem
Message
Dispatcher
Transport
Mapping
User-based
Security
Model
Other
Security
Model
UDP
IPX
Other
. . .
Network

## Slide 67: SNMP Entity - Agent
Message Processing
Subsystem
v1MP
v2cMP
PDU
Dispatcher
otherMP
v3MP
Security
Subsystem
Message
Dispatcher
Transport
Mapping
User-based
Security
Model
Other
Security
Model
UDP
IPX
Other
. . .
Network
Access Control
Subsystem
View-based
Access Control
Model
Other
Access Control
Model
Command
Responder
Proxy
Forwarder
Notification
Originator
MIB Instrumentation

## Slide 68: SNMPv3 - Message Structure
msgVersion
msgID
msgMaxSize
msgFlags
msgSecurityModel
msgAuthoritativeEngineID
msgAuthoritativeEngineBoots
msgAuthoritativeEngineTime
msgUserName
msgAuthenticationParameters
msgPrivacyParameters
contextEngineID
contextName
PDU
Scoped PDU
(plaintext or
encrypted)
Generated/
Processed by
User Security
Model (USM)
Generated/
Processed by
Message
Processing
Model
scope of authentication
scope of encryption

## Slide 69: Serialization
Internet
Data Link
Transport
Application
Node A
Node B
?
1100 0111 0101 11
1010 1001 0010 01
1100 0111 0101 00
1010 1001 0010 01

## Slide 70: BER – Tag Field 1(2)
Class
Constructed
Tag number
8 7 6 5 4 3 2 1
Tag format
Constructed - primitive(0) or constructed(1)
Class
Bit 8
Bit 7
Comment
Universal
0
0
Built-in types
Application
0
1
SNMP defined types
Context-Specific
1
0
Used in context
Private
1
1
Not used in the SNMP protocol
Tag
Length
Value

## Slide 71: BER – Tag Field 2(2)
Type
ASN.1 Tag
Tag Number
Tag Value
INTEGER
0x02
OCTET STRING
0x04
NULL
0x05
OBJECT IDENTIFIER
Universal 6
0x06
0x02
0x04
0x05
0x06
Universal 5
Universal 4
Universal 2
SEQUENCE
0x10
IpAddress
0x00
Counter32
0x01
Gauge32, Unsigned32
Application 2
0x02
0x30
0x40
0x41
0x42
Application 1
Application 0
Universal 16
TimeTicks
0x03
Counter64
0x04
Context-Specific
0x06
noSuchObject exception
Context-Specific 0
0x00
0x43
0x44
0x46
0x80
Application 6
Application 4
Application 3
noSuchInstance exception
0x01
endOfMibView exception
0x02
0x81
0x82
Context-Specific 2
Context-Specific 1
Tag Numbers

## Slide 72: BER – Length Field 1(2)
Short/Long form indicator
Length value
8 7 6 5 4 3 2 1
Short Length form (max 127 byte)
Tag
Length
Value

## Slide 73: BER – Length Field 2(2)
Short/Long form indicator
Length of length field
8 7 6 5 4 3 2 1
Long Length form (> 127 byte)
Length value
Tag
Length
Value

## Slide 74: BER – Value Field
Sign bit - plus(0), minus(1)
8 7 6 5 4 3 2 1
INTEGER (-128...127)
Send 2
Examples
Send -2
Invert all
Add 1
Send this
Tag
Length
Value

## Slide 75: BER – SNMPv1 Message
len
Sequence of fields
0x30 - sequence
tag
len
tag
len
tag
len
tag
Community
Version
Seq.of fields
0x02 - integer
0x04 - octet string
depends on PDU
(0xa0 - get-request)
len
tag
len
tag
len
tag
Err-stat
Req. ID
Err-ind
0x02 - integer
0x02 - integer
0x30 - sequence
0x02 - integer
len
tag
Seq. of Var-bind
len
tag
Pair of fields
0x30 - sequence
len
tag
Pair of fields
0x30 - sequence
….
len
tag
ID
0x06 - object identifier
len
tag
Value
depends on type of value

## Slide 76: SNMP – Exercise 1(5)
30
1.3.6.1.2.1.1.7
sysServices
Floor 1
1.3.6.1.2.1.1.6
sysLocation
ior.easysoft.se
1.3.6.1.2.1.1.5
sysName
nisse hult
1.3.6.1.2.1.1.4
sysContact
25920000
1.3.6.1.2.1.1.3
sysUpTime
1.3.6.1.4.1.9.1.3
1.3.6.1.2.1.1.2
sysObjectID
Cisco Internet..
1.3.6.1.2.1.1.1
sysDescr
Value
Object ID
Object Name
OID
Oper
Value
1. Get sysName
SNMP Manager
SNMP Agent (System Group)

## Slide 77: SNMP – Exercise 2(5)
30
1.3.6.1.2.1.1.7
sysServices
Floor 1
1.3.6.1.2.1.1.6
sysLocation
ior.easysoft.se
1.3.6.1.2.1.1.5
sysName
nisse hult
1.3.6.1.2.1.1.4
sysContact
25920000
1.3.6.1.2.1.1.3
sysUpTime
1.3.6.1.4.1.9.1.3
1.3.6.1.2.1.1.2
sysObjectID
Cisco Internet..
1.3.6.1.2.1.1.1
sysDescr
Value
Object ID
Object Name
OID
Oper
Value
2. Get sysLocation (use GetNext)
SNMP Manager
SNMP Agent (System Group)

## Slide 78: SNMP – Exercise 3(5)
aa 00 04 00 09 40
1.3.6.1.2.1.2.2.1.6
ifPhysAddress
10000000
1.3.6.1.2.1.2.2.1.5
ifSpeed
1500
1.3.6.1.2.1.2.2.1.4
ifMtu
6
1.3.6.1.2.1.2.2.1.3
ifType
Ethernet0
1.3.6.1.2.1.2.2.1.2
ifDescr
1
1.3.6.1.2.1.2.2.1.1
ifIndex
2
1.3.6.1.2.1.2.1
ifNumber
Value
Object ID
Object Name
OID
Oper
Value
3. Find out the number of interfaces
SNMP Manager
1544000
1500
22
Serial0
2
0
1.3.6.1.2.1.2.2.1.22
ifSpecific
…
…
…
25915000
1.3.6.1.2.1.2.2.1.9
ifLastChange
1
1.3.6.1.2.1.2.2.1.8
ifOperStatus
1
1.3.6.1.2.1.2.2.1.7
ifAdminStatus
0
…
13183000
1
1
*
SNMP Agent (Interfaces Group)

## Slide 79: SNMP – Exercise 4(5)
aa 00 04 00 09 40
1.3.6.1.2.1.2.2.1.6
ifPhysAddress
10000000
1.3.6.1.2.1.2.2.1.5
ifSpeed
1500
1.3.6.1.2.1.2.2.1.4
ifMtu
6
1.3.6.1.2.1.2.2.1.3
ifType
Ethernet0
1.3.6.1.2.1.2.2.1.2
ifDescr
1
1.3.6.1.2.1.2.2.1.1
ifIndex
2
1.3.6.1.2.1.2.1
ifNumber
Value
Object ID
Object Name
OID
Oper
Value
4. Find out operational status for all interfaces
SNMP Manager
SNMP Agent (Interfaces Group)
1544000
1500
22
Serial0
2
0
1.3.6.1.2.1.2.2.1.22
ifSpecific
…
…
…
25915000
1.3.6.1.2.1.2.2.1.9
ifLastChange
1
1.3.6.1.2.1.2.2.1.8
ifOperStatus
1
1.3.6.1.2.1.2.2.1.7
ifAdminStatus
0
…
13183000
1
1
*

## Slide 80: SNMP – Exercise 5(5)
aa 00 04 00 09 40
1.3.6.1.2.1.2.2.1.6
ifPhysAddress
10000000
1.3.6.1.2.1.2.2.1.5
ifSpeed
1500
1.3.6.1.2.1.2.2.1.4
ifMtu
6
1.3.6.1.2.1.2.2.1.3
ifType
Ethernet0
1.3.6.1.2.1.2.2.1.2
ifDescr
1
1.3.6.1.2.1.2.2.1.1
ifIndex
2
1.3.6.1.2.1.2.1
ifNumber
Value
Object ID
Object Name
OID
Oper
Value
5. Shutdown interface 2
SNMP Manager
SNMP Agent (Interfaces Group)
1544000
1500
22
Serial0
2
0
1.3.6.1.2.1.2.2.1.22
ifSpecific
…
…
…
25915000
1.3.6.1.2.1.2.2.1.9
ifLastChange
1
1.3.6.1.2.1.2.2.1.8
ifOperStatus
1
1.3.6.1.2.1.2.2.1.7
ifAdminStatus
0
…
13183000
1
1
*