## Slide 1: 7. Network Monitoring
Objectives
Monitor Health Status
Event Action
Hands On

## Slide 2: Monitor Health Status using SNMP
Status Tests from NMS based on:
- status changes
- thresholding
Traps from devices based on:
- status changes
- thresholding
- events
Trend Reports based on:
- manual thresholding
- baseline thresholding
- TopN reports

## Slide 3: Monitor Health Status not using SNMP
TCP Port Tests based on:
- SYN/SYN-ACK
- String response
Transaction Tests based on:
- SMTP/POP3, FTP etc.
- Logon scripts
- Response Time
- …

## Slide 4: Link Test – Hands on 1(2)
Monitor interface status between :
a) uplink_switch2 and switch2
b) switch2 and router2
- poll nearest node
- check slot/port connection (cdp)
- find index number (ifIndex)
- setup a status test on ifOperStatus.x

## Slide 5: Link Test – Hands on 2(2)
- select the link between uplink_switch2 and switch2
- right click and do the following changes:
- cont. with 1.b)

## Slide 6: DHCP Test – Hands on
Monitor free addresses in scoope 192.10.20.0
- OK threshold value > 5
- setup the test on device Jupiter
- NB! table indexing is subnetAdd

## Slide 7: Event Action
How to react on:
- Regular Polls (ping)
- SNMP based Status Test
- Non-SNMP based Status Test
- Traps from device
- Trend Report alarms
- ….
All is Traps!
- action is controlled by filters

## Slide 8: Event Action – Hands on
3. Insert filters for Link Tests:
- one filter for pollStatusTestFail
- one filter for pollStatusTestPass
- change Message to: is $’2
- match on alarmVariable: *ifOper*
- test the new filters by acknowledge the
link events in current log (right click)