## Slide 1: 1. Introduction
Objectives
SNMP History
IETF Standards
Field of Applications
RMON
NetFlow

## Slide 2: What is Network Management ?
Fault detection
Monitoring
Traffic analysis
Security
Provisioning
Performance analysis
IP-handling (DHCP/DNS)
Configuration of network elements
…

## Slide 3: Network Management
Areas according to ISO 7498-4
F – Fault Management
C – Configuration Management
A – Accounting Management
P – Performance Management
S – Security Management

## Slide 4: Why Network Management ?
Demand for accessibility
Information spread out
Growing networks

## Slide 5: Why SNMP ?
Different kind of equipments
Multiple Vendors
Cisco
HP
Extreme
3Com
Ericsson
D-Link
Microsoft

## Slide 6: Successful ?
Troubleshooting
Backup
Configuration
Performance
Monitoring
SNMP
Telnet/CLI
Web/Http
FTP/Script

## Slide 7: Alternatives to SNMP
DMTF Distributed Management Task Force
        In the beginning PC (DMI)
        CIM; data model (WMI)
CLI-script CLI-based script
        TCL, Telnet, Perl, Python etc.
CORBA Common Object Request Broker Architecture
        Telecom worlds
WS Web Services
        Methods, WDSL, XML, SOAP

## Slide 8: Its hard to be a vendor
Can we use the Web interface today?
SNMP Agent
Telnet Server
Web Server
FTP Server
(CORBA)
Web Services?

## Slide 9: More focus on funtionality
Do we have any problems today?
One single interace (SNMP)
Funtionality

## Slide 10: SNMP – History 1(6)
1987 Three proposals
  HEMS (High-level-Entity Management System)
  SGMP (Simple Gateway Monitoring Protocol)
  CMOT (CMIP over TCP)
1988 Feb IAB is setting up a working group
  Instructions; a solution now
1988 Apr Report from the working group
  SNMP in the short perspective
  CMOT in the long perspective

## Slide 11: SNMP – History 2(6)
1988 Aug Proposal to SNMP version 1
  RFC 1065: SMI (the structure)
  RFC 1066: MIB (a number of objects)
  RFC 1067: SNMP (the protocol)
1990 May SNMPv1 raised to Standard/Recommended
  RFC 1155: new SMI
  RFC 1156: new MIB
  RFC 1157: new SNMP

## Slide 12: SNMP – History 3(6)
1991 Mar Introducing Traps
  RFC 1212: concise MIB format
  RFC 1215: Trap format
1991 Aug MIB-II raised to Standard/Recommended
  RFC 1213: extention of MIB (RFC 1156)

## Slide 13: SNMP – History 4(6)
1993 Apr Proposal to SNMP version 2
  RFC 1441-1452
1996 Jan SNMPv2 Draft Standard/Elective
  RFC 1902-1908
1998 Jan Proposal to SNMP version 3
  RFC 2271-2275

## Slide 14: SNMP – History 5(6)
1999 Apr SNMPv3 Draft Standard/Elective
  RFC 2571-2575
1999 Apr SMIv2 Standard/Recommended
  RFC 2578-2580

## Slide 15: SNMP – History 6(6)
2002 Mar SNMPv3 Standard/Recommended
  RFC 3410: Introduction
  RFC 3411: Architecture
  RFC 3412: Message Processing
  RFC 3413: SNMP Applications
  RFC 3414: Security (USM)
  RFC 3415: Access Control (VACM)
  RFC 3416: Protocol Operations
  RFC 3417: Transport Mappings
  RFC 3418: MIBs
2003 Nov SNMPv1 Historical

## Slide 16: SNMP versions – The Protocol 1(2)
SNMPv1 - RFC 1157 (historical)
- security based on ”community names”
- 5 protocol operations
SNMPv2p - RFC 1441, 1445, 1446, 1448, 1449 (historical)
- security based on ”parties”
- 2 new protocol operations
SNMPv2c - RFC 1901, 1905, 1906 (exp. + draft standard)
- security based on ”community names”
- 2 new protocol operations

## Slide 17: SNMP versions – The Protocol 2(2)
SNMPv2u - RFC 1905, 1906, 1909, 1910 (draft std. + exp.)
- security based on ”users”
- 2 new protocol operations
SNMPv2* - Not def. in RFC’s (experimental)
- security based on ”users”
- 2 new protocol operations
SNMPv3 - RFC 3410-3418 (standard)
- security based on ”users”
- 2 new protocol operations

## Slide 18: SNMP versions – The Structure
SMIv1 - RFC 1155, 1212, 1215 (standard)
SMIv2 - RFC 2578-2580 (standard)
- extended definitions
- table handling
- one new data type

## Slide 19: The Standardisation Process 1(4)
 | Req. | Rec. | Elec. | Lim. | Not
Standard |  |  |  |  | 
Draft Std. |  |  |  |  | 
Prop. Std. |  |  |  |  | 
Inform |  |  |  |  | 
Experim |  |  |  |  | 
Historical |  |  |  |  | 
STATUS
S
T
A
T
E
IESG
IETF WG

## Slide 20: The Standardisation Process 2(4)
 | Req. | Rec. | Elec. | Lim. | Not
Standard |  |  |  |  | 
Draft Std. |  |  |  |  | 
Prop. Std. |  |  |  |  | 
Inform |  |  |  |  | 
Experim |  |  |  |  | 
Historical |  |  |  |  | 
STATUS
S
T
A
T
E
IESG
IETF WG
SNMPv1

## Slide 21: The Standardisation Process 3(4)
 | Req. | Rec. | Elec. | Lim. | Not
Standard |  |  |  |  | 
Draft Std. |  |  |  |  | 
Prop. Std. |  |  |  |  | 
Inform |  |  |  |  | 
Experim |  |  |  |  | 
Historical |  |  |  |  | 
STATUS
S
T
A
T
E
IESG
IETF WG
SNMPv2

## Slide 22: The Standardisation Process 4(4)
 | Req. | Rec. | Elec. | Lim. | Not
Standard |  |  |  |  | 
Draft Std. |  |  |  |  | 
Prop. Std. |  |  |  |  | 
Inform |  |  |  |  | 
Experim |  |  |  |  | 
Historical |  |  |  |  | 
STATUS
S
T
A
T
E
IESG
IETF WG
SNMPv3

## Slide 23: IETF Working Groups
Application Area
General Area
Operations and
Management Area
General Area
Routing Area
Security Area
Transport Area
User Service Area

## Slide 24: Operations and Management 1(2)
Area Director(s): Bert Wijnen, David Kessens
  Authentication, Authorization and Accounting
  ADSL MIB
  Benchmarking Methodology
  Bridge MIB
  Control And Provisioning of Wireless Access Points
  Distributed Management
  Domain Name System Operations
  Entity MIB
  Global Routing Operations
  Ethernet Interfaces and Hub MIB
  Internet and Management Support for Storage

## Slide 25: Operations and Management 2(2)
cont.
  IP over Cable Data Network
  IP Flow Information Export
  MBONE Deployment
  Site Multihoming in IPv6
  Network Configuration
  Operational Security Capabilities for IP Network Infrastructure
  Packet Sampling
  RADIUS EXTensions
  Resource Allocation Protocol
  Remote Network Monitoring
  Configuration Management with SNMP
  IPv6 Operations

## Slide 26: SNMP Managers
Flat Organization
NMS
Hierarcial Organization
NMS
NMS
NMS

## Slide 27: SNMP Agents
SNMPv1
SNMPv1/v2c
SNMPv1/v2c/v3
Proxy Agent
Extensible
Master Agent
Sub Agent
MIB
MIB
MIB
MIB
Sub Agent
Sub Agent
MIB
MIB
MIB
- SMUX, RFC 1227
- DPAPI, RFC 1592
- EMANATE, SNMP Research
- Microsoft SNMP API
- AgentX, RFC 2741
NMS
MIB

## Slide 28: AgentX
Master Agent
Sub Agent
MIB
Sub Agent
Sub Agent
MIB
MIB
MIB
- initiate session to master-agent
- register their MIB-area
- sends and receives AgentX messages
- MIB instrumentation
- initiate Trap events
NMS
- accept session from sub-agent
- accept registration of MIB-area
- sends and receives AgentX messages
- supports adm. MIB-objects (RFC 2742)
- manage access control of MIB-views
- sends and receives SNMP messages
RFC 2741

## Slide 29: Monitoring
”The Real World”
NMS

## Slide 30: Event Triggering 1(2)
90%
75%
time
disk usage
event threshold
rearm threshold
Edge Triggered Events

## Slide 31: Event Triggering 2(2)
90%
time
disk usage
event level
Level Triggered Events
clock period

## Slide 32: Fault Detection
NMS

## Slide 33: Configuration
NMS

## Slide 34: Trend Reports
NMS
RMON

## Slide 35: Remote Monitoring (RMON)
Index | Packets | BrdCast | MultiCast | CRC
1 | 24010 | 25 | 5 | 2
2 | 14034 | 26 | 4 | 1
3 | 12035 | 25 | 4 | 1
4 | 29120 | 30 | 3 | 5
5 | 35023 | 25 | 3 | 2
Result Table
Index | Packets | BrdCast | MultiCast | CRC
1 | 24010 | 25 | 5 | 2
2 | 14034 | 26 | 4 | 1
3 | 12035 | 25 | 4 | 1
4 | 29120 | 30 | 3 | 5
5 | 35023 | 25 | 3 | 2
DataSource | BucketsReq | Interval
1 | 50 | 30
1 | 50 | 1800
Control Table
RMON
RMON
RMON-1
RMON-2
OSI

## Slide 36: RMON-1
Ethernet statistics (1)
Ethernet history (2)
Alarm (3)
Host (4)
HostTopN (5)
Matrix (6)
Filter (7)
Packet capture (8)
Event (9)
TokenRing (10)

## Slide 37: RMON-2
Protocol directory (11)
Protocol distribution (12)
Address mapping (13)
Network layer host (14)
Network layer matrix (15)
Application layer host (16)
Application layer matrix (17)
User history (18)
Probe configuration (19)

## Slide 38: NetFlow
Traffic analysis without probes
Developed by Cisco
  IOS 12.03(T) (1999)
Network level (routers)
Proposed IETF Standard
  RFC 3955 (Oct 2004)

## Slide 39: What is a Flow ?
7 unique keys
  Source IP address
  Destination IP address
  Source port
  Destination port
  Layer 3 protocol type
  TOS byte (DSCP)
  Input logical interface (ifIndex)
Traffic
UDP Export
Packets
Application GUI
Enable NetFlow

## Slide 40: NetFlow Benefits
Service Provider
  Peering Arrangements
  Network Planning
  Traffic Engineering
  Accounting and Billing
  Security Monitoring
Enterprise
  Internet Access Monitoring
  User Monitoring
  Application Monitoring
  Security Monitoring

## Slide 41: NetFlow versions
Cisco (and others)
  1 Original
  5 Standard and most common
  7 Specific to 6500 and 7600 switches
  8 Aggregation schemes
IETF (IPFIX)
  9 Flexible, extensible export format

## Slide 42: Data Export
Expired flows are grouped together into “Netflow Export” UDP datagrams for export to a collector
UDP is used for speed and simplicity
NetFlow Cache
Header
Sequence number
Record count
Version number

## Slide 43: Flow Ageing
When is a flow expired?
  Transport is completed (TCP FIN or RST)
  After 15 sec of traffic inactivity (the only way for UDP). The inactive timer
  After 30 min of traffic activity. The active timer
  The cache is becoming full

## Slide 44: NetFlow Summary
Not a switching path
7 flow identifiers
For ingress traffic only
A flow is unidirectional
IP unicast only